SPH-3.0 Pre-Mix Heater

Bidding Specifications

1.0 INTENT

It is the intent of this specification to provide for the purchase of one (1) new and unused portable asphalt storing, heating and dispensing box to be used for the purpose of maintaining proper working temperature of hot mix asphalt.

The following specification is based upon a Stepp Mfg Portable SPH3.0 Hot Box Premix Heater. The Public Works Department has evaluated different styles of asphalt hotbox equipment and has determined that this product is best suited for the DPW needs in terms of quality and features.  This specification shall not be interpreted as restrictive but rather as a measure of quality and performance against which all other Portable Hot Box Premix Heaters will be compared.

In comparing proposals, comparison will not be confined to price only.  The successful bidder will be one whose product is judged as best serving the interests of the DPW when price, product, quality and delivery are considered. The DPW also reserves the right to reject any or all bids or any part thereof, and to waive any minor technicalities. A contract will be awarded to the bidder submitting the lowest responsible bid meeting the requirements.

2.0 EQUIVALENT PRODUCT

Bids will be accepted for consideration on any make or model that is equal or superior to the hot box specified.  Decisions of equivalency will be at the sole interpretation of the DPW.  A blanket statement that equipment proposed will meet all requirements will not be sufficient to establish equivalence. An original manufacture’s brochure of the proposed product is to be submitted with proposal.

3.0 INTERPRETATIONS

In order to be fair to all bidders, no oral interpretations will be given to any bidder, as to the meaning of the specification documents or any part thereof.  Every request for such a consideration shall be made in writing.  Based on such inquiry, the DPW may chose to issue an Addendum in accordance with local state laws.

4.0 GENERAL

The specification herein states the minimum requirements of the DPW. All bids must be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The DPW will consider as irregular or nonresponsive any and all bids that are not prepared and submitted in accordance with the bid document and specification, or any bid lacking sufficient technical literature to enable the DPW to make a reasonable determination of compliance to the specification.  It shall be the bidders responsibility to carefully examine each item of the specification. Failure to offer a completed bid or failure to respond to each section of the technical specification (COMPLY: YES NO) will cause the proposal to be rejected without review as non responsive. All variances, exceptions and/or deviations shall be fully described in the appropriate section. Deceit in responding to the specification will  be cause for rejection.

5.0 SPECIFICATIONS

COMPLY

HOPPER:									YES	NO

Unit shall be portable, trailer mounted 					____	____

Frame shall be constructed of welded steel					____	____

Frame shall meet or exceed all DOT safety regulations			____	____

Length shall not exceed 208” inches 						____	____

Width shall not exceed 90"							____	____

Height shall not exceed 90”							____	____

Weight shall be approximately 4,500. lbs. (including trailer)		____	____

Minimum storage capacity shall be 3.0cy					____	____

Walls shall be minimum triple wall construction				____	____

Wall insulation shall be minimum 2” of 1½# density hi-temperature

fiberglass.									____	____

Outer shell construction shall be a minimum 16 gauge thick steel		____	____

Inner hopper walls shall be minimum 12 gauge				____	____

Heat jacket diffuser shall be constructed of 309 stainless steel and have

an adjustable heat baffle.							____	____

Frame shall be constructed of high strength rectangular steel tubing 	____	____

Frame shall be reinforced at all stress points					____	____

Frame tubing shall have a minimum thickness 2”x 6”x 3/16” 		____	____

6.0 Loading Doors

Top loading doors shall be covered with a minimum of 16 gauge steel	____	____

Top load doors shall utilize gas assist shocks with lock downs		____	____

Loading doors shall be insulated with 3” closed-cell polyurethane foam 	____	____

Loading doors of tapered design with water lip to allow water shedding	____	____

7.0 Heating System								YES	NO

Shall be constructed with an air jacketed heating system			____	____

Air jacket shall be engineered to evenly transfer heat and prevent

scorching.									____	____

Hot air shall exhaust into the hopper, providing heat over the top of the

mix pile 									____	____

Shall use center heat riser to bring heat to center preventing asphalt

bridging									____	____

Minimum burner capacity shall be minimum 105,000 BTU			____	____

Burner shall be diesel fueled							____	____

Shall include a forced air burner system manufactured by Beckett Corp	____	____

Burner system shall feature electronic spark ignition and blower		____	____

Burner system shall offer flame-out shutdown				____	____

Burner to be mounted at the front of the unit, away from operator		____	____

Burner shall be easily accessible and removable				____	____

Burner system operations shall be controlled at operator station		____	____

8.0 Discharge

Shovel platform shall be constructed of 1/4” 304 Stainless Steel		____	____

Hot box shall include minimum of two rear discharge doors 		____	____

Discharge doors shall include gas assist opening system for easy

open/close	 								____	____

Discharge doors shall not require latches or hooks to hold open		____	____

Design shall have sloped inner walls to move mix forward to allow easy

shovel  									____	____

9.0 Controls

Controls shall be safely located at the rear of the unit closest to the curb	____	____

9.0 Controls (continued)							YES	NO

Control box shall feature:
     A) Automatic Temperature Controls 1/32 Din.				____	____

B) Burner On/Off Switch							____	____

C) Digital Electronic Temperature Gauge					____	____

D) Thermostat for hotbox							____	____
     F) Controls for OPTIONAL Strobe light or arrow stick controls 		____	____

10.0 Trailer

Trailer shall be municipal tandem axle					____	____

Trailer shall have electric brakes with break away kit			____	____

Hitch shall be pintle style ring						____	____

Trailer shall be fitted with height adjustable hitch minimum range

21” - 34”									____	____

Axles shall be a minimum 7000LB each.					____	____

Suspension shall be leaf spring type 						____	____

Shall have screw jack with minimum 5,000LB Capacity			____	____

Fenders shall be heavy duty miminum12 gauge steel bolt on design		____	____

Tires shall be ST235/80/R16 with steel welded wheel.			____	____

Minimum tire specifications shall be load range E radial tire		____	____

Trailer electrical system shall be 12 volt DC battery with charging circuit.	____	____

Turn signals and stop lights shall be sealed beam grommeted.		____	____

Side markers shall be mounted at the rear and sides of the unit		____	____

Safety Chains shall be grade 40, attached eye bolts.				____	____

11.0 Available Options - Shall Include:					YES	NO

OPTION- Tack Tank:

Unit will be equipped with a heated tack tank with a minimum capacity

of 40 gallons with 3% expansion.  						____	____

Shall be rectangular in shape. Vertical tack tanks will not be accepted.	____	____

To have a 6"fill cap.  Diesel bottom fired configuration. Will have a 2"

molasses gate valve for draining the tank. 					 ____	____

Heated tack tank to be insulated with 2" of 1 1/2# hi-temperature

fiberglass insulation with 16 gauge outside cover. 				____	____

The thermostat shall have a digital readout that displays both set

and actual product temperature and be adjustable from 0-550ºF.		____	____

Optional Pumping System for Tack Tank:

To include a 12 hp, 2 Cylinder, liquid cooled, Kubota diesel engine with

electric start.									____	____

A 12 volt battery shall be included and located in a lockable battery box.

The engine shall power a hydraulic pump. 					____	____

The hydraulic pump shall power a hydraulic motor which will operate a

Viking HL-32 material pump.  Pump shall be capable of forward and

reverse positions.  								____	____

To include 15' of yellow ortec hose and 5' steel spray wand with an

on/off valve.  A 3-way valve shall be installed to allow for flushing of

pump and plumbing.								____	____

Compactor Plate Carrier:

Compactor Plate Carrier with hydraulic raise and lower for operator

convenience and shall have a spring lock and fold up out of the way

when not in use.								____	____

Electric Overnight Heat:

Shall have 110 Volt over night heaters. 2-750 watt 110 VAC heater to

heat and maintain material temperatures for cold mix materials

over night.									____	____

Shovel Cleaning Compartment:
Shall have a Shovel Cleaning Compartment constructed of 12 gauge

material with splash guard compartments, drain plug, and rain tight

cover. Shall hold (4) four shovels.						____	____

Tool Box:
12”x12”x24” Steel Tool Box.							____	____

Tool Holders:

(2) Stainless Steel Tool Holders-spring loaded clamps mounted

on each fender for holding rakes, shovels and lutes.				____	____

Arrow Stick:

Optional arrow stick for increased operator safety. Mounted on the top

rear of hopper with controller in the operators control panel.		____	____

Strobe Light:

Optional Flashing LED Light; Beacon or Flush mount.			____	____

LP Hand Torch:

20# LP Bottle with hand torch and bottle rack.				____	____

Surge Type Brakes:

Surge type brakes in lieu of Electric Brakes.					____	____

Hose Reel:

Hose reel for tack hose and/or hand torch.					____	____

Lighting Options:

Standard 2 Light System:							____	____

2 Light LED System:								____	____

4 Light System:								____	____

4 Light LED System:								____	____

Diesel Burner Enclosure:

Lockable enclosure to protect burner from outside elements, also

vandal proof.									____	____

Spare Tire:

To include (1) 235/80/R16 tire and mounting bracket.			____	____

Front Platform with Railing:

Shall be constructed of formed, stamped, grip strut material, to include

hand rail.									____	____

Wacker WP1550AW Plate Compactor:

19.5 x 23 plate  compactor with water tank for asphalt compaction.		____	____

Battery Charger:

To include (1) 12 volt type battery charger to maintain batteries in unit. 	____	____

12.0 Paint									
To be primed with primer and painted highway black unless otherwise

specified. Paint to be a 2 part poly urethane paint minimum 6 mils thick.	____	____

13.0 Warranty

13.1 Manufacturer’s warranty shall be a minimum of 1 year			____	____

14.0 Delivery

Equipment shall be furnished fully assembled, serviced and quality

checked 									____	____

Two operator and parts manuals shall be furnished with the unit		____	____

Unit shall be delivered to DPW’ US facility as indicated			____	____

Acceptance shall be subject to inspection and approval of the DPW		____	____

Bidder shall state delivery time  ________________ Days (ARO) After Receipt of Order.

Exceptions & Deviations

Bidder shall fully describe every variance exception and/or deviation.  List the item number here and fully explain any items in non-compliance with specification.   Additional sheets may be used if required.

________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Price for (1) SPH 3.0 Pre-mix Heater or Equal

$_______________________ (FOB DESTINATION)

Bidding Company _____________________________________________

Address______________________________________________________

City, State, Zip ________________________________________________

PH:_________________________FX:_______________________

Authorized Representative______________________________________

Signature_____________________________________________________

Date:_______________________

Email:_____________________________________