STPH 4.0 Hook Mounted

Bidding Specifications

1.0 INTENT

It is the intent of this specification to provide for the purchase of one (1) new and unused Hook Style Asphalt Heater to be used for the purpose of maintaining proper working temperature of hot mix asphalt.

The following specification is based upon a Stepp Mfg STPH 4.0 Hook Style Premix Heater. The Public Works Department has evaluated different styles of asphalt hotbox equipment and has determined that this product is best suited for the DPW needs in terms of quality and features.  This specification shall not be interpreted as restrictive but rather as a measure of quality and performance against which all other Hook Style Premix Heaters will be compared.

In comparing proposals, comparison will not be confined to price only.  The successful bidder will be one whose product is judged as best serving the interests of the DPW when price, product, quality and delivery are considered. The DPW also reserves the right to reject any or all bids or any part thereof, and to waive any minor technicalities. A contract will be awarded to the bidder submitting the lowest responsible bid meeting the requirements.

2.0 EQUIVALENT PRODUCT

Bids will be accepted for consideration on any make or model that is equal or superior to the hot box specified.  Decisions of equivalency will be at the sole interpretation of the DPW.  A blanket statement that equipment proposed will meet all requirements will not be sufficient to establish equivalence. An original manufacture’s brochure of the proposed product is to be submitted with proposal.

3.0 INTERPRETATIONS

In order to be fair to all bidders, no oral interpretations will be given to any bidder, as to the meaning of the specification documents or any part thereof.  Every request for such a consideration shall be made in writing.  Based on such inquiry, the DPW may chose to issue an Addendum in accordance with local state laws.

4.0 GENERAL

The specification herein states the minimum requirements of the DPW. All bids must be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The DPW will consider as irregular or non-responsive any and all bids that are not prepared and submitted in accordance with the bid document and specification, or any bid lacking sufficient technical literature to enable the DPW to make a reasonable determination of compliance to the specification.  It shall be the bidder’s responsibility to carefully examine each item of the specification. Failure to offer a completed bid or failure to respond to each section of the technical specification (COMPLY: YES NO) will cause the proposal to be rejected without review as non responsive. All variances, exceptions and/or deviations shall be fully described in the appropriate section. Deceit in responding to the specification will be cause for rejection.

5.0 SPECIFICATIONS

HOOK MOUNTED:								YES	NO

Unit shall  be equipped with a hook truck hitch to allow the addition of

other types of equipment.							____	____

HOPPER:

Hopper shall have a capacity of 4 cubic yard.				____	____

The hopper shall have an overall dimension of 101” long

56” high and 96” wide. The inner tank shall have a slope of 32º.		____	____

Triple wall construction, inner hopper to be constructed of 10 gauge

material. 									____	____

Oil jacketed chamber to be constructed of 10 gauge material insulated

with 2" of 1½# density hi-temperature fiberglass insulation. The oil tank

Shall have 150 gallons of heat transfer oil minimum.			____	____

The unit shall have 2 lateral heat baffles designed into the hopper to

help evenly distribute heat into the center of material. The baffles shall

have heat transfer oil circulated through them. Insulation covers to be 16

Gauge.										____	____

Hopper shall be covered with two (2) 16 gauge hydraulically operated

doors.  										____	____

The doors shall open a full 270º to allow full hopper access for filling

while having the lowest overall height. Doors shall open with hydraulic

driven gear boxes. Door shall be double walled and insulated with 3”of

insulation.									____	____

Door operation will be controlled from rear curb side of unit and a

warning buzzer will sound during door operations. 				____	____

Material will be delivered to the rear of the unit by means of an auger.

The material is discharged onto a shovel platform or directly onto

the repair site on the roadway. 						____	____

The shoveling platform shall fold up to allow material to be dispensed

on the road way. The platform will have a lock to lock the platform in

up position.									____	____

The auger will be 6" diameter with hardened flighting and hardened

auger trough. Auger flighting shall be 3/8”thick by 6” diameter

AR (abrasion resistant) steel.							____	____

Auger will be powered by a 2 speed 32 cubic inch hydraulic motor with

forward and reverse capability. 						____	____

To be controlled from rear curb side of unit.  Auger shaft will be coupled

to the hydraulic motor by a flexible coupling to allow for movement. Support

bearing to be 1½” with permanently lubricated ball bearings with

hi-temperature seals.			  					____	____

Hopper shall have a thermostat in the hopper to monitor the temperature

of the material. 								____	____

Temperature gauges to be digital and be intergraded into the thermostat

control and shall monitor product temperature and heat transfer oil

temperature and optional tack tank.						____	____

Constructed with side mounted storage compartments for tool storage.	____	____

HEATING SYSTEM FOR HOPPER:					YES	NO

Unit will be equipped with a 12 Volt Beckett Diesel Burner with up to

490,000 BTU output, firing into a 12” heating chamber transitioning

down to a 6” x .188 fire tube.							____	____

Heat transfer oil shall surround the sides and bottom of hopper and

circulate thru heat risers for even material heating.  The fire tube will

run from along the bottom of the oil jacket and return to a vertical

stack exhausting into the top of the hopper to reduce bridging.		____	____

Equipped with automatic temperature control, spark ignition with flame

sensing for automatic shut down of main diesel burners in case of flame

out. To be equipped with all necessary fittings, hoses and valves. 		____	____

The flue will be equipped with one (1) replaceable 309 stainless steel

diffuser to prevent hot spots in heating chamber. 				____	____

The diesel burner fuel is supplied from the on board  fuel tank.		____	____

A hydraulic operated heat transfer oil pump shall be included to

circulate the hot oil evenly around the hopper for even heating.		____	____

HYDRAULIC SYSTEM:							YES	NO

Hopper shall utilize hydraulic pump from the hook system on the truck.

A manifold shall be installed in between the hydraulic pump and the

trucks valve to operate the hook system. The manifold will have 3

hydraulic quick connectors for the pressure line, return line and the load

sense line. This will allow both hydraulic valves, hopper and hook, to

operate simultaneously.				  			____	____

Hopper shall have hydraulic controls for discharge auger, hot oil

circulating pump, and top cover. 						____	____

Valve to be a Force America Add-A-Fold. The valve sections shall be rated

at 20GPM. The hydraulic valve shall be of modular manifold design.  Each

hydraulic function requires an individual manifold stacked together to form

the manifold base.  The manifold base shall consist of an inlet section with

SAE #16 inlet porting, SAE #20 outlet  porting, and SAE #4 load sense

porting.  There shall be a main system relief in the inlet section to protect

the system from high pressure in case the pump compensators fail.  Each

hydraulic valve segment shall be individually mounted to the manifold base

assembly and be serviceable without removing any hydraulic hoses or any

other hydraulic valve segments.  Each hydraulic valve segment shall have

individual pressure compensation to achieve independent simultaneous

operations.  All segments shall have heavy-duty continuous duty coils

and connections shall be with Din connectors.  All coils shall operate

at 12 VDC and require a maximum of 1400 mille-amps.  Each segment

shall be equipped with a manual overrides.  					____	____

All hydraulic lines to be run in steel tubing with face seal fittings.		____	____

All hydraulic functions shall be operated from operators control panel.	____	____

LIGHTS:									YES	NO

Lights will be seal beam style. Rubber grommet mount. All lighting

shall meet state and federal regulations of the FMVSS. 			____	____

Unit will have 7 rear facing lights.						____	____

Stop, tail, turn and clearance lights will be mounted in the fenders.		____	___

Three light bar to be mounted on the top of the rear discharge door

assembly.									____	____

PAINT:									YES	NO

To be primed with primer and painted highway black unless otherwise

specified. Paint to be a 2 part poly urethane paint minimum 6 mils thick.	____	____

WARRANTY:								YES	NO

One (1) year on workmanship and manufactured equipment.  		____	____

Available Options:							YES	NO

HOPPER ACCESS WALKWAYS

Shall have front and rear built-in steps with a fold down hopper access

platform with raised grip tread and non-skid surface.			____	____

SHOVEL CLEANING COMPARTMENT:

Shall have a Shovel Cleaning Compartment constructed of 12 gauge

material with splash guard compartments, drain plug, and cover.

Shall hold (4) four shovels. 							____	____

Reciprocating Air Compressor

Shall be powered from the truck hydraulic system. Air compressor shall

Be used to clean debris from potholes. Shall have 25 cfm rating		____	____

Air Blast System

Shall be equipped with air that is supplied to an auxiliary tank by

The truck air compressor to enable operator to provide a short blast

Of air to clean out small potholes.						____	____

A safety valve shall be incorporated into the air system to prevent loss

Of air to the air brake system							____	____

Shall include 25’of 3/8” air hose with blow stick handle			____	____

WASH DOWN SYSTEM:

Wash down System with a 12V.D.C. pump with application hose and

wands for cleaning tools and hopper. Shall be pumped from truck fuel

tank and interfaced with burner shutoffs when the wash down is in

operation			.						____	____

HOSE REELS FOR WASH DOWN:

Spring rewind hose reels for wash down hose. 				____	____

WHELEN SUPER LED LIGHT SYSTEM:

Shall have a WHELEN SUPER LED Light Package which includes 2 mirror

mount strobes, stop, tail, turn , back up, 2 rear strobes and clearance lights.

All LED								.	____	____

TACK TANK:

Unit shall have an 80 gallon tack tank integrated into the hopper.		____	____

Tack system to be driven hydraulically and have a heat transfer oil

heating system that is thermostat ally controlled. 				____	____

DIESEL BURNER w/AUTO TEMP FOR TACK TANK:

Unit to include diesel burner. The thermostat shall have a digital readout

that displays both set and actual product temperature and be adjustable

from 0-550ºF.									____	____

PUMPING SYSTEM FOR TACK TANK:

Shall include a hand wand which shall be 48”x ½” and equipped with a

Vee-jet nozzle with fan spray. 						____	____

Wand shall have a twist style shut off valve due to spring or dead man

valves not operating with sticky asphalt material. 				____	____

Sprayer hose to be 15’x ½” and system to have solvent flushing

capabilities.									____	____

Spray system to operate from rear curb side of the machine with a

re-circulating port to allow product to circulate back to tank.		____	____

Asphalt pump shall be a positive displacement 10 GPM self-priming

pump. 										____	____

The pumping system shall have a WPC (wand pressure control valve)

In place of relief valve. Relief valves do not function properly with

asphalt materials due to the sticky nature of the material. The WPC

valve adjusts wand pressure and relieves pressure when wand is off.	____	____

COMPACTOR PLATE CARRIER:

Compactor Plate Carrier with hydraulic raise and lower for operator

convenience and shall have a spring lock and fold up out of the way when

not in use.									____	____

SPOILS BIN:

Shall include a Spoils Bin constructed of 10 gauge steel with trap door

in bottom. Capacity of 6 cubic feet located on right side of unit in front

of rear axle.									____	____

OVERNIGHT ELECTRIC HEATER:

Allows for a faster start-up and helps to maintain heat. The hopper shall

have 2-3000 watt, 230 V.A.C, connected to the same thermostat as the

diesel heater and wired to a 10'-8 gauge extension cord for overnight

heating. The tack tank, when included, shall have 1-1500 watt heater

wired to the same thermostat as the tack tank.				____	____

ARROWSTICK:

Optional arrow stick for increased operator safety. Mounted on the top

rear of hopper with controller in the operators control panel.		____	____

STROBE LIGHTS:

Optional Flashing Beacon							____	____

LED TRUCK LIGHTS:

LED Lights TRUCK Lights in lieu of grommet incandescent Lights	____	____

HOSE REELS:

Spring rewind hose reels for tack hose, lp hand torch hose and wash

down hose. 									____	____

Exceptions & Deviations

Bidder shall fully describe every variance exception and/or deviation.  List the item number here and fully explain any items in non-compliance with specification.   Additional sheets may be used if required.

_______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________